1-wire (onewire) master

Abbreviations, terminology and product names
Verilog HDL	Verilog hardware description language
RTL	register transfer level
SoC	system on chip
FPGA	field-programmable gate array
ASIC	application-specific integrated circuit
HAL	hardware abstraction layer
OS	operating system
μC/OS-II	preemptive, real-time deterministic multitasking kernel written in ANSI C
1-wire (onewire)	single wire serial bus protocol
Quartus II	FPGA design and synthesis tool from Altera
SOPC Builder	system on a programmable chip builder
Nios II EDS	Nios II (32-bit softcore processor from Altera) embedded development suite
Avalon MM	Avalon memory mapped switch fabric interface
Wishbone	open source hardware computer bus

# Introduction
This document describes a 1-wire master written in Verilog HDL, ready for integration into a FPGA or ASIC based SoC. A port of the 1-wire Public Domain Kit (version 3.10r2) from Maxim is also provided, with all the code required for integration into the Altera development environment.
## 1-wire protocol and devices
The 1-wire protocol was defined by Dallas Semiconductor. In 2001 the company was bought by Maxim Integrated Products, Inc. Maxim is the main manufacturer of 1-wire and iButton devices. Devices and standards can be found on their web-page http://www.maxim-ic.com/products/1-wire/.
## Features
Only the physical layer of the protocol is implemented in hardware, so only bit level data transfers are possible, a software driver or hardware state machine is required to perform byte level transfers and to support higher protocol layers. Features:
1. reset pulse generation and presence detection, bit level write and read, timed idle cycle
2. overdrive mode
3. from 1 to 16 wires (4 wires for an 8bit interface)
4. power (strong pull-up)
5. polling or interrupt driven CPU interface
There are no special features, like active pull-up or adaptive timing, for handling a long and unstable bus.
## List of source files
The sources can be divided into Verilog RTL and testbench code, C code for drivers, code required for integration into Altera development tools and documentation.
Table 1: File list
file name	description
doc/onewire.odt	this document (onewire.odg contains source drawings)
hdl/onewire_tb.v	Verilog testbench
hdl/onewire_slave_model.v	Verilog model of 1-wire slave device (very simplified)
hdl/sockit_owm.v	main module Verilog RTL source
hdl/wishbone2bus.v	Wishbone to bus protocol converter Verilog RTL source
sockit_owm_hw.tcl	Script for integrating the hardware into Altera dev. tools
sockit_owm_sw.tcl	Script for integrating the software into Altera dev. tools
inc/sockit_owm_regs.h	C header file describing CPU bus accessible registers
HAL/inc/sockit_owm.h	C header file for Nios II HAL integration
HAL/src/owlnk.c, ...	C source code ported from the 1-wire Public Domain Kit

# Verilog module parameters and ports
The next section describes how to properly integrate the Verilog module into a SoC.
## Parameters
The next list of parameters is almost complete, but there are some timing parameters that should be modified only by developers able to read the HDL source code.
Table 2: List of sockit_owm module parameters
parameter	type	default	range (8bit interface)	description
OVD_E	integer	1	0, 1	overdrive functionality enable
CDR_E	integer	1	0, 1	clock divider register enable
BDW	integer	32	32 (8)	bus data width
OWN	integer	1	1, 2, ..., 16 (4)	number of wires
BTP_N	string	"5.0"	"7.5", "5.0", "6.0"	base time period for normal mode
BTP_O	string	"1.0"	"1.0", "0.5"	base time period for overdrive mode
CDR_N	integer	15	0, 1, ..., 65535 (255)	clock divider ratio for normal mode
CDR_N	integer	2	0, 1, ..., 65535 (255)	clock divider ratio for overdrive mode

### Optional functionality
If overdrive mode is not required it can be disabled (OVD_E=0).
If the input clock is constant, clock divider ratios can be implemented as constant parameters (CDR_E=0) instead of registers (DCR_E=1).
### Data bus width, number of wires and overdrive enable
The width of the data bus is 32bit by default. An 8bit bus option is provided for connecting to to a 8bit CPU, but this restricts the number of 1-wire line to 4 (OWN<=4). The details are explained in the section on module ports.
For 32 bit CPU interfaces if is possible to have from 1 to 16 wires. Note that only one wire can be active at the same time. If simultaneous data transfers on more than one wire are required, one solution would be to instance more than one sockit_owm module, but this would require a software driver modification.
### Clock divider ratio and base time periods
The internal state machine requires a base time period. For normal mode the base can be exactly 7.5μs or 5.0μs, or in the range from 6.0μs to 7.5μs. For overdrive mode the base can be 1.0μs or in the range from 0.5μs to 0.66μs. The system clock frequency must be such that it is possible to divide it into the desired period. If overdrive is enabled, both normal and overdrive mode periods must be achievable. Exact time periods offer a better optimized implementation, range periods should be used only if a round frequency is not possible.
Table 3: Base time period and base frequency options
overdrive support (OVD_E)	disabled			enabled
base time period [μs] (normal mode)	7.5	5	6.0 - 7.5	7.5	5.0	6.0 - 7.5
base time period [μs] (overdrive mode)				1.0	1	0.5 - 0.66
base frequency [Mhz]	0.13	0.2	0.166 - 0.133	2	1	2 - 1.5

The clock divider ratio parameters (register values) are computed with the next formulas (replace the base period as required):
"CDR_N" = f_{clk} cdot 7.5 {%mu}s - 1
"CDR_O" = f_{clk} cdot 1.0 {%mu}s - 1
And the exact base time period is computed as:
"BTP_N" = {"CDR_N"+1} over f_{clk}
"BTP_N" = {"CDR_N"+1} over f_{clk}
If the dividing factor is not a round integer, than the timing of the controller will be slightly off, and would support only a subset of 1-wire devices with timing closer to the typical 30μs base. If the relative error is large (this is possible if the system clock frequency is low) than range periods should be used. For range periods longer times (closer to the higher limit) offer a better signal quality, although a lower data rate.
## Ports
Module ports are divided into two groups: CPU bus ports and 1-wire interface ports.
Table 4: List of sockit_owm module ports
signal	width	direction	description
bus_wen	1	input	bus write request
bus_ren	1	input	bus read request
bus_adr	BAW*	input	bus address
bus_wdt	BDW	input	bus write data
bus_rdt	BDW	output	bus read data
bus_irq	1	output	bus interrupt status
owr_i	OWN	input	1-wire bus status
owr_e	OWN	output	1-wire open collector driver enable
owr_p	OWN	output	1-wire power enable (strong pullup)

* for a 32 bit interface BAW=1, for an 8bit interface BAW=2
### CPU bus interface
The default bus interface is 32bit Avalon MM compatible. It is trivial to connect it to Wishbone (wishbone2bus module) and it should be easy to connect to AMBA APB. The module can be also connected to an 8bit bus (a micro-controller for example).
Table 5: Wishbone equivalents of Avalon MM signals
bus signal	Avalon MM signal	Wishbone signal
bus_wen	avalon_write	cyc & stb & we
bus_ren	avalon_read	cyc & stb & ~we
bus_adr	avalon_address	adr
bus_wdt	avalon_writedata	dat_w
bus_rdt	avalon_readdata	dat_r
bus_irq	avalon_interrupt	irq

All CPU related signals are active high. Both read and write cycles are a single clock period long, the omitted Avalon MM signal bus_waitrequest would be a constant '0'. Read data is valid only the first cycle of bus_ren being active, it might change in the next cycle due to the interrupt status being cleared.
The interrupt signal indicates, that a reset (with presence detection) or a read/write bit 1-wire cycle has finished. After reading the control/status register the interrupt is cleared.

Drawing 1: Bus timing (write, read cycle and interrupt status)

clk
bus_wen
bus_ren

bus_wdt
bus_rdt
bus_irq

bus_adr

### 1-wire interface
The 1-wire module requires an external open drain driver to be able to drive a bidirectional pin. The owr_p signal can be used to supply extra power to the 1-wire line (for temperature conversion, ...), if the signal is not used, 0 should be applied instead. The next scheme shows the driver for the i-th line.

Drawing 2: 1-wire line driver schematic

owr_p[i]
owr_p[i] | owr_e[i]
owr_i[i]
owr[i]
The next Verilog code should be used for the i-th line on the top level of the SoC.
assign owr [i] = (owr_p[i] | owr_e[i]) ? owr_p[i] : 1'bz;
assign owr_i[i] = owr;

And if the power signal is ignored.
assign owr [i] = owr_e[i] ? 1'b0 : 1'bz;
assign owr_i[i] = owr;

On some FPGA it is possible to set driver strength at compile time. There are no extra features for long 1-wire networks, but it is suggested to use weak drivers (slow slew rate) to minimize transitional effects on the network. If the FPGA pin is to be used to provide power to an 1-wire slave, the opposite, to use strong drivers is suggested. If both requirements are present the user must choose the proper compromise based on testing.
## Metastability evaluation
The 1-wire line is samples at the presence detection point for reset cycles and at the data sample point for read/write data cycles. The sampled value is stored in a register and at the end of the 1-wire cycle copied into a register visible on CPU interface data bus. The time shortest time between the sampling and being available on the bus is 5μs, this is enough for all metastability problems to level out.
# Supported 1-wire functionality
The sockit_owm module provides timed cycles for 1-wire reset/presence and write/read bit for both normal and overdrive mode. This section describes how the 1-wire link layer is implemented by the sockit_owm module RTL.
## RTL description
The core of the RTL is a state machine with a 7bit or 8bit counter. On each bus write the counter and owr signals are set to appropriate values. The clock generator provides pulses every base time period (depends on overdrive mode being used), on each pulse the counter is decremented and the owr signals are changed as required. More details can be found in the RTL source.

Drawing 3: RTL block diagram

power
select
control
/
status

owr_e

state
machine

7/8bit
counter

owr_i

owr_p

clk
bus_wen
clock generator

ovd

pls

bus_ren
bus_rdt
rst
dat

bus_wdt
bus_irq

bus_adr

cdr_n

cdr_o

irq
cyc
## 1-wire cycle timings
The timing for 1-wire cycles is defined as a set of minimum and maximum values for certain cycle segments. In case the master is the data source (reset and write) the minimal values are optimal since they provide the fastest transfer rate. In case the slave is the data source (presence and read) the maximum values are optimal since they allow the signal to stabilize as much as possible.

Table 6: 1-wire protocol standard timing restrictions
timing / [μs]	normal		overdrive		optimal	description
	min	max	min	max
tRSTL	480	640	48	80	min	reset low
tRSTH	480	∞	48	∞	min	reset high (on newer devices this time is lower)
tRSTP	60 / +8.1	75	6 / +1.3	10	max	reset presence detect / (the extra delay is due to slow slave IO)
tDAT0	60	120	6	16	min	data bit 0
tDAT1	5	15	1	2	min	data bit 1
tDATS		15		2	max	data sample
tREC	5	∞	2	∞	min	recovery
tDLY					1ms	idle delay (not standard, about tRSTL+ tRSTH)
tRSTT	960	∞	69	0		reset pulse cycle (tRSTL+ tRSTH)
tDATT	61	121	7	17		read/write slot cycle (tDAT0+ tREC)

The exact timing of 1-wire cycles is provided as a table with 3 options for normal mode and 2 options for overdrive mode. For exact base time periods only typical values are provided, for range base time periods minimum and maximum value are provided.
Table 7: Timing options
	normal mode times [μs]					overdrive mode times [μs]
name	"7.5"		"5.0"		"6.0"			"1.0"		"0.5"
timing	N	typ	N	typ	N	min	max	N	typ	N	min	max
base	1	7.5	1	5	1	6	7.5	1	1	1	0.5	0.66
tRSTL	64	480	96	480	80	480	600	48	48	96	48	64
tRSTH	64	480	96	480	80	480	600	48	48	96	48	64
tRSTP	10	75	15	75	10	60	75	10	10	15	7.5	10
tDAT0	8	60	12	60	10	60	75	6	6	12	6	8
tDAT1	1	7.5	1	5	1	6	7.5	1	1	2	1	1.33
tDATS	2	15	3	15	2	12	15	2	2	3	1.5	2
tREC	1	7.5	1	5	1	6	7.5	2	2	4	2	2.66
tDLY	128	960	200	1000	160	960	1200	96	96	192	96	128

The 7.5ns cycle period option is also explained with timing diagrams.
The reset cycle is 128 periods long. Reset low and high time each take 64 periods. After the rising edge on the wire a typical 1-wire slave would assert its presence after 4 periods (min 2, max 8), and keep it asserted for 16 periods (min 8, max 32). The presence status is sampled when most stable at 10 cycles after the reset rising edge.

Drawing 4: Reset timing diagram
tRSTT

127...

tRSTS

...64
...0
63...

tRSTL
tRSTH

The write '0' cycle is 9 periods long. The wire is tight low for 8 periods than released. The recovery time is 1 period.

Drawing 5: Write 0 timing diagram

8
7
6
5
4
3
2
1
0

tREC

tDATT
tSLOT = tLOW0
The write '1' or read cycle is 9 periods long. The wire is tight low for 1 period than released. A typical 1-wire slave would answer with '0' by holding the wire down for 4 periods (min 2, max 8) from the falling edge of the read command. Data is sampled at the most stable point at 2 periods from the falling edge. There is 1 period at the end for recovery.

Drawing 7: Write 1, read timing diagram

8
7
6
5
4
3
2
1

0

tDATS
tLOW1
tREC

tDATT
tSLOT

Drawing 6: Write 1, read timing diagram

8
7
6
5
4
3
2
1

0

tDATS
tLOW1
tREC

tDATT
tSLOT

# Processor interface
The processor interface is described in three steps:
1. address space
2. clock dividers
3. 1-wire line multiplexing and power enable functionality
4. control/status register description
5. driver access sequences (pooling and interrupts)
The document is focused on describing the 32bit CPU interface. Some aspects of a 8bit interface are mentioned, but many details are omitted.
## Address space
The sockit_own module is designed to be accessible by a 32bit CPU through a single 32bit register, if between 1 and 16 (OWN parameter) 1-wire lines are required. If a single line is enough than all but one power and select bits have no function, and the interface can be compacted into an 8bit control/status register.
If implemented (CDR_E=1), there are two 16bit clock divider ratio registers (cdr_n, cdr_o) one for normal and one for overdrive mode.
Table 8: 32bit interface address space
address	31..24	23..16	15..8		7..0
0	power			select	control/status
1	cdr_o		cdr_n

Since all the controls are in a single register and there is no byte select signal, on every write all controls must have the correct value. In software this can be achieved by having a permanent structure holding the interface current state.
Alternatively an 8bit interface is possible. The maximum number of 1-wire lines is reduced to 4 and the clock divider ratio register size is reduced to 8bit.
Table 9: 8bit interface address space
address	7..0
0	control/status
1	power		select
2	cdr_n
3	cdr_o

## Clock dividers
If clock divider ratio registers cdr_n and cdr_o are implemented (CDR_E=1) than the reset value of the registers will be as defined by CDR_N and CDR_O parameters, and the registers can be written to with new divider ratios while there is no 1-wire cycle in progress. If the registers are not implemented (CDR_E=0) than a read will provide values defined by parameters and writes will be ignored.
## 1-wire line multiplexing and power enable
The sockit_owr module can implement more than one 1-wire line depending on the value of the OWN parameter. The main purpose of having multiple lines is the ability to attach sensors (thermometers for example) to separate lines, so that the physical position of the sensor can be deduced without requiring sensors with addressing or chain structures.
Since there is a single state counter in the module, it is not possible to communicate with more than one device at the same time. To be exact only one contemporary reset or write/read bit cycle can be issued, but it is possible to time multiplex between lines on bit transfer level. Each cycle must finish before a new cycle on the same or different line can be issued.
The select[3:0] register is used to select one from OWN lines. If the module is configured for only one line (OWN=1), than select is not implemented and therefore ignored. If a line is not selected its owr_e signal is not active. After reset line 0 is selected, but the proper value has to be provided on each write to the register.
The power[15:0] register is directly connected to the owr_p[OWN-1:0] output port. If the module is configured for only one line (OWN=1), than power[15:0] is not implemented and ignored and the pwr bit from the control/status register is used instead. If the module is configured for more than one line (OWN=1) than writes to the pwr bit are ignored. After reset all bits in the register are zero and all lines are only powered over the required weak pull-up resistor. By writing 1 into the n-th bit the n-th 1-wire line will provide power supply instead of being only an input. While power to a line is enabled it is not possible to perform 1-wire cycles on the same line, but it is possible to communicate on other lines.
## Control/status register
The control/status register is used to initiate 1-wire cycles and to check their status.
Table 10: Control/status register structure
	7	6	5	4	3	2	1	0
name	ien	irq	/	pwr	cyc	ovd	rst	dat
access	r/w	r/c	/	r/w	r/w	r/w	r/w	r/w
reset	0	0	x	0	0	0	0	x

Table 11: Control/status register bits with descriptions
bit		description
0	dat	write: data transmit request (0 - perform write 0 slot, 1 - perform write 1 or/and read slot) / read: data receive status (read value for each 1-wire read slot) / read: presence detect status (0 - device presence detected, 1 - no device detected)
1	rst	reset pulse request (0 - no action, 1 - reset and read presence detect cycle is selected)
2	ovd	overdrive setting (0 - standard speed, 1 - overdrive speed)
3	cyc	write: initiate an 1-wire cycle / read: 1-wire cycle status (0 - no cycle, 1 - cycle in progress)
4	pwr	power supply (0 - normal operation, 1 - supply power over 1-wire)
5	/	reserved
6	irq	status of cycle interrupt (set on end of 1-wire cycle, cleared by bus read)
7	erx	enable cycle interrupt (0 - disabled, 1 - enabled)

Bits ovd, rst, dat are used to configure a cycle and bit cyc is used to start it. Bit dat provides the write data, bit rst selects a reset cycle and bit ovd is used to specify the transfer speed mode. Combinations of this three bits are used to select 8 different cycle types (see table below, timing values are for normal mode "5.0" and overdrive mode "1.0" base time periods). Detailed timing for this cycles is explained in the section "Supported 1-wire functionality".
Writing '1' into cyc register will always initiate an 1-wire cycle. Writing '1' into the register while a cycle is already in progress will break the running cycle and start a new cycle, usually causing a protocol error. When read cyc shows the cycle status, which can be used for polling.
Table 12: List of supported cycles
ovd	rst	dat	timing	description
0	0	0	65μs	write '0' cycle
0	0	1	65μs	write '1' cycle or read cycle
0	1	0	960μs	reset and presence detect cycle
0	1	1	1000μs	timed idle cycle, can be used to generate timed delays
1	0	0	8μs	overdrive write '0' cycle
1	0	1	8μs	overdrive write '1' cycle or read cycle
1	1	0	96μs	overdrive reset and presence detect cycle
1	1	1	0μs	zero time idle cycle, can be used to change power settings

Bit pwr has a different meaning for write than for read. The write functionality is only implemented if only a single 1-wire line is implemented (OWN=1). The write value directly controls the status of the owr_p[0] signal. Read of pwr provides state of the selected line power (power[select] or pwr).
Read only bit irq describes the current interrupt request status and is set at the end of each 1-wire cycle. Interrupt status is cleared by a register read, so care must be taken to check its value on every read. Bit ien (interrupt enable) specifys if irq will trigger an interrupt or not.
## Driver access sequences
The 1-wire master can be used to perform most actions defined in the iButton specification as the physical layer. It is possible to use pooling or interrupts, both options will be described.
The reference implementation for Nios II HAL and μC/OS-II is available as source code.
The description uses the next pseudo functions:
- write (data) - 32bit (or 8bit) write to the configuration/status register
- data = read () - 32bit (or 8bit) read from the configuration/status register
If clock divider ratio registers are implemented (CDR_E=1) they must be written with proper divider ratios prior to issuing any 1-wire cycles.
Note that the provided pseudo code does not implement power delivery and is designed for a single 1-wire lane (select is not used). For a proper implementation of this functionality see the ported public domain kit code (owlnk.c).
### Polling routines
Polling is not an optimal implementation, but it might be useful for debugging purposes. Since interrupts are not used '0' should be written into interrupt enable register and cycle status bit cyc is used to identify the end of the cycle.
Two basic functions are provided one for reset pulse and the other for a combined write/read data slot. Separate write and read data functions are based on the combined data slot function.
#### Reset and presence pulses
A '1' is written into the rst bit and a '0' is written into the dat bit. Bit ovd is used to select normal or overdrive mode. The cycle will start after writing '1' into cyc. The software must wait in a loop till the cycle ends (cyc=0), and than the presence status can be read from bit dat. The next function returns the presence detect status.

bool owr_reset (bool overdrive)
{
  int reg;
  write (0x8 | (overdrive << 2) | 0x02);
  while ((reg = read()) & 0x08);
  return (reg & 0x01);
}
#### Read/write data slots
A boolean value bit is written into the txd bit, this will cause a write bit cycle on the 1-wire bus. Bit ovd is used to select normal or overdrive mode. The cycle will start after writing '1' into cyc. The software must wait in a loop till the cycle ends (cyc=0), and than the read bit can be read from status register bit dat. The next function returns the read bit.

bool owr_slot (bool bit, bool overdrive)
{
  int reg;
  write (0x8 | (overdrive << 2) | bit);
  while ((reg = read()) & 0x08);
  return (reg & 0x01);
}

Read data bit and write data bit functions are based on the slot function.
bool ovd_read (bool overdrive) {return owr_slot (0x1, overdrive);}
void ovd_write (bool bit, bool overdrive) {owr_slot (bit, overdrive);}
#### Delay of 0ms or 1ms

bool owr_reset (bool overdrive)
{
  int reg;
  write (0x8 | (overdrive << 2) | 0x02);
  while ((reg = read()) & 0x08);
  return (reg & 0x01);
}

### Interrupt routines
The 1-wire protocol is slow compared to clock speeds of most embedded processors, even low poser micro-controllers. Because of the low speed the a pooling driver might spend many CPU cycles (at leas 7 for bit read/write and 960 for the reset pulse) busy waiting for the 1-wire cycle to finish, this time could be better spent performing useful tasks. To be able to use this idle time a task scheduler (usually provided by an operating system) is also required, so that there can be alternative threads that can be executed while waiting for the interrupt (or waiting for temperature conversion to finish).
Since the 1-wire bus can be accessed from more than one task, a locking mechanism is required, so that higher level protocol sequences are not corrupted. Only locking of low level transfers is described here. Locking for higher protocol layers is provided by the "public domain kit".
The provoded pesudocode is for a pseudo OS, to implement the driver for a real OS, many OS specific details related to task and IO scheduling must be taken into account. The OS must provide the next functions (and others for initialization):
- os_sem_lck (sem) - lock the resource (it becomes unavailable to other tasks)
- os_sem_rel (sem) - release the resource lock
- os_io_wait (flag) - return the CPU back OS, wait for IO data for flag to be available
- os_io_done (flag) - tell the OS IO data for flag is available, this will end the wait
The main detail to be careful about is interrupt status bits being cleared by bus read.
#### Reset and presence pulses, read/write data slots
The functions for reset pulses and data slots are similar to the polling versions. The busy wait while loop is replaced with the os_io_wait function that returns the CPU to the OS and waits for an IO event (interrupt) when the CPU is returned to the 1-wire driver. The 1-wire cycle is also wrapped into a semaphore based lock preventing a different task from disrupting the cycle.

bool owr_reset (bool overdrive)
{
  os_sem_lck (sem);
  write (0x8 | (overdrive << 2) | 0x02);
  os_flag_wait (flag);
  os_sem_rel (sem);
  reg = ;
  return (read() & 0x01);
}

bool owr_slot (bool bit, bool overdrive)
{
  os_sem_lck (sem);
  write (0x8 | (overdrive << 2) | bit);
  os_flag_wait (flag);
  os_sem_rel (sem);
  return (read() & 0x01);
}

#### OS initialization and interrupt service routine
The HAL or OS must declare and initialize the semaphore and flag and register the interrupt service routine.

os_type_sem sem;
os_type_flag flag;

os_create_sem (sem);
os_create_flag (flag);

os_irq_register (irq_sockit_owm);

The interrupt service routine must clear the interrupt (by reading the status register) and using the flag signal the OS that the wait for data has ended.

void irq_sockit_owm ()
{
  read();
  os_io_done (flag);
}

# Software driver
A port of the Public Domain Kit (version 3.10r2) to Nios II HAL and μC/OS-II real time OS is available with the sockit_owr component. This section describes this port, and how it can be extended.
## Public Domain Kit components to Nios II HAL and μC/OS-II
The port is done based on instructions from Altera and Maxim.
### Nios II HAL and μC/OS-II drivers
The integration into Nios II software development environment is done with a TCL script and C source and header files. The integration is done based on instructions from Altera.
Table 13: files for Nios II HAL and μC/OS-II integration
file	description
sockit_owm_sw.tcl	TCL script for integration into Nios II EDS
inc/sockit_owm_regs.h	specification of hardware registers and low level access macros
HAL/inc/sockit_owm.h	initialization and interrupt handling code
HAL/src/sockit_owm.c

The TCL script provides integration into the Nios II EDS, by defining:
- driver version and compatibility
- list of C sources and headers
- list of driver configuration options
The register definitions are mostly used for initialization and interrupts related code and for the 1-wire protocol link layer. The next IO macros are provided for reading from and writing into the control/status and clock divider ratio registers:
IORD_SOCKIT_OWM_CTL(base)
IOWR_SOCKIT_OWM_CTL(base, data)
IORD_SOCKIT_OWM_CDR(base)
IOWR_SOCKIT_OWM_CDR(base, data)

Interrupt support is provided for a system without or with the μC/OS-II real time OS. But there are no advantages using interrupts if there is no task scheduling implemented on the system. Since the sockit_owm module provides only bit sized data transfers, there are interrupt for each bit. If the CPU is running at low clock speeds, the operating system overhead might be substantial.
### Public Domain Kit components
The public domain kit provides a layered 1-wire protocol implementation. The focus of the port was on layers common to all 1-wire devices, device drivers with the exception of thermometers were omitted. Support for other devices and applications have to be ported separately.

The ported files were located in the next directories from the Public Domain Kit package:
- owpd310r2/common - some common code (CRC, err, findtype) and device drivers
- owpd310r2/apps/temp - the thermometer demo application is from here
- owpd310r2/doc - documentation
- owpd310r2/lib/general - data link and session layer TODO files
- owpd310r2/lib/general/shared - transport and network layer files
Table 14: files from the Public Domain Kit
file	description
HAL/inc/ownet.h	main protocol stack header file
HAL/src/owlnk.c	1-wire protocol data link layer functions
HAL/inc/ownet.c	1-wire protocol network layer functions
HAL/src/owtran.c	1-wire protocol transport layer functions
HAL/src/owses.c	1-wire protocol session layer functions
HAL/src/owerr.c	1-wire driver error handling
HAL/src/crcutil.c	1-wire protocol CRC utilities
HAL/inc/findtype.[hc]	1-wire network search for devices
HAL/inc/temp10.[hc]	thermometer device driver (ID 0x10 - DS1920/DS1820)
HAL/inc/temp28.[hc]	thermometer device driver (ID 0x28 - DS18B20)

Most code changes were done to owlnk.c and owses.c. Some platform specific code for unrelated platforms was removed from . Other files are mostly unchanged, check the Git repository to see details.
## Adding support for new devices
Support for a new device can be added by copying needed files from the /common directory in the public domain kit into the working directory of the Nios II project. Applications can also be ported from the /apps directory.
## Possible improvements
The main limitation the user has to be careful with is only one hardware module instance can be handled by the driver. This due to how the public domain kit handles ports (1-wire lines). The current driver select the a port by providing it as in integer input into functions. To be able to drive more than one hardware instance, a structure (as defined for Nios II HAL) should be used instead of an integer. Since this method is used in almost all high level functions in the public domain kit, there would be too many changes necessary to enable multiple instances.
So a possible improvement would be to rewrite the public domain kit to have a structure instead of an integer for the portnum variable.
# Altera development tools integration
The sockit_owm component can be used in any FPGA, but special care has been taken integrating it into the Altera development tools environment. The directory sockit_owm can be used as a portable component for easy integration into an Altera FPGA design.
## SOPC Builder and Nios II EDS integration
Integration is done according to Altera specification with two TCL scripts.
- sockit_owm_hw.tcl for SOPC Builder integration
- sockit_owm_sw.tcl for Nios II EDS integration
### SOPC Builder
#### Adding the component to a project
SOPC builder component IP search path must point to the directory containing the sockit_owm directory. The easiest way to achieve this is to put sockit_owm into the directory of the Quartus II project and add the project directory to the search path. Use this menu path:
SOPC Builder > Tools > Options > IP Search Path > Add ...
Once the proper IP search path is set, the module will be available under:
Library > Interface Protocols > Serial > 1-wire (onewire)
#### Configuring the component
The next configuration options are available in the component GUI:
- OVD_E enable overdrive mode implementation
- CDR_E enable clock divider ratio register implementation
- OWN select the number of implemented 1-wire lines
- BTP_N base time period for normal mode
- BTP_O base time period for overdrive mode
Overdrive mode can be disabled (OVD_E=0) in case devices that only support normal mode will be used. Disabling overdrive mode implementation provides a small reduction in logic consumption.
For low-end and midrange devices the clock frequency is usually defined at compile and fixed during runtime, so there is no need for software to change values of clock divider ratio registers. If the registers are not implemented (CDR_E=0) the divider values are constant. Disabling clock divider ratio registers implementation provides a small reduction in logic consumption.
The number of 1-wire lines can be set with OWN. Although many 1-wire devices can be connected to the same line there are usage scenarios where the device can be identified by the line it is connected to. An example would be more than one thermometer on the same circuit board.
It is possible to change the base time period for normal and overdrive mode mode, although the default is usually appropriate.
The TCL script calculates the correct clock divider ratios automatically based on the system clock frequency and base time periods. The script also reports deviations from ideal values and if the error is more than 2% an error event is generated.

Illustration 1: sockit_owm component GUI
### Nios II EDS
The C driver is integrated into the BSP automatically if a SOPC Builder project containing the sockit_owm component is used to generate the BSP.
The driver requires some application code to use the driver. An example application is present in the demo. Device driver files from the public domain kit can be added to the project and device drivers already included in the base driver can be disabled within BSP configuration tools.
The user can configure the driver with some options, but the default values should be appropriate for most projects. This options are translated into define macros and can be enabled or disabled within BSP configuration tools.
Table 15: Driver configuration options
option	default	description
SOCKIT_OWM_POLLING	disabled	use polling instead of interrupts
SOCKIT_OWM_HW_DLY	enabled	use the delay slot in hardware instead of usleep
SOCKIT_OWM_ERR_ENABLE	enabled	enable the error code from the public domain kit
SOCKIT_OWM_ERR_SMALL	enabled	small version of the error implementation

# Demo hardware and software implementation
The popular Terasic DE1 demo board is used for a demo implementation. 1-wire devices can be connected to the PS2 port. The demo software is using the JTAG UART to communicate with the user.
This section also provides hardware logic an software memory sizes.
## Demo hardware
The demo project is a Nios II SoC with 8MiB SDRAM for software and JTAG UART for communication with the Nios II EDS. Two 1-wire lines are connected to the PS2 connector.

Illustration 2: image of the PS2 connector on the Terasic DE1 board
The PS2 connector is used since it provides a 5V power supply and the signals already have 2kΩ pull-up resistors (required to implement the 1-wire bus) and 120Ω series resistors (usefull for preventing damage to the board). The DATA and CLK pins are used to connect the two 1-wire lines.
Table 16: pin-out of the PS2 connector on the Terasic DE1 board
pin	name	description
1	OWR[0]	1-wire line 0 with a 2kΩ pull-up to 5V and 120Ω serial resistor to the FPGA pin
2	NC	not connected
3	GND	ground
4	VCC	+5V power supply
5	OWR[0]	1-wire line 1 with a 2kΩ pull-up to 5V and 120Ω serial resistor to the FPGA pin
6	NC	not connected

1-wire devices can be connected to the two lines in any combination. A single DS1820 or DS18B20 thermometer in TO92 package can even be directly inserted into the PS2 connector.
### Demo hardware logic consumption
The demo hardware has the default parameters ("5.0" and "1.0" base time periods, no clock divider registers) except for the 2 1-wire lines. This configuration implemented inside an Altera Cyclone II device running at 48MHz consumes 66 combinatorial LC and 26 LC registers.
To fit inside smaller devices like CPLDs with few logic cells the next steps can be taken:
- implement a single lane, so select and power registers will not be implemented
- lower the clock frequency, so a smaller clock divider is required
- disable overdrive mode
- use the 8bit bus width option
- fix the bus address to 0, so read of clock divider ratios will not be implemented
- use the "7.5" base time period, this should reduce the state machine size
- do not use the interrupt signal
## Demo software

Temperature device demo:

(0) 3F000000C8CF9B28 22.3 Celsius
(1) 44000801E51EC510 22.8 Celsius

Press any key to continue

# Testing
The sockit_owm component was tested on two levels. The Verilog RTL was tested in simulation and the C driver was tested on the demo implementation.
## Verilog RTL tests
Since the RTL module can be used separately from the provided C driver (with a Linux kernel driver for example) and can be implemented in an ASIC, so extensive testing is required.
Table 17: Verilog RTL testbench files
file	description
hdl/onewire_slave_model.v	1-wire slave with parameterizable timing and debug features
hdl/onewire_tb.v	Verilog testbench
sim/iverilog_gtkwave.scr	Bash script for running the bench with RTL parameter options
sim/iverilog_gtkwave.cmd	Windows cmd script
sim/gtkwave.sav	GTKWave save file

### 1-wire slave model
The Verilog 1-wire slave model onewire_slave_model.v is based on the assumption that 1-wire devices have an internal time base (probably implemented with a RC oscillator) on which an internal state machine is running.
For normal mode this time base is typically Ttyp=30μs, but can vary from a minimum of Tmin=Ttyp/2=15μs on fast devices to a maximum of Tmax=Ttyp*2=60μs on slow devices. This assumptions are based on the the 1-wire protocol specification mentioning that the fastest device is 4 times faster than the slowest device.
For overdrive mode the typical time base seems to be Ttyp,o=Ttyp/8=3.75μs. The tolerances for devices supporting overdrive mode seem to be more strict, and on the fast side. So for fast devices Tmin,o≈16μs/8=2μs and for slow devices Tmax≈48μs/8=6μs.

Drawing 8: 1-wire slave model timing diagram
T

read '0'
write '0'
reset
presence

8T
T

4T
0
1
3
4
2
5

6
1-wire slave model timing diagram check points are assumptions based on the 1-wire timing from the standard.
0 - the 1-wire master pulls the line low
    for a read slot the slave pulls the line low if read data is '0'
1 - for a write slot the slave samples data from the line state
    for a read slot the slave releases the line
2 - the slave samples reset status from the line state
3 - the master releases the line at the end of reset low time
4 - the slave pulls the line low to indicate its presence
5 - the slave releases the line
### Verilog testbench
The bench code is separated into two parts, a Verilog testbench for RTL internals and a Bash script for parameters.
The Verilog testbench tests for the RTL logic and 1-wire timing. The logic tests are:
- CPU bus access
- clock dividers
- 1-wire state machine
- overdrive mode
- power delivery
1-wire timing tests are performed on three 1-wire slave models with different timings: minimum (2 times faster than typical), typical and maximum (2 times slower than typical). This should ensure that the timing from the protocol are implemented correctly. The next 1-wire cycles are tested:
- reset pulse
- write/read '0'/'1'
- 1ms delay pulse
- 0ms idle pulse
With each test data transfers in both directions are checked (presence detection, read from slave, write to slave) and power delivery status is also checked.
### Parameter tests
A Bash script is used to run the testbench with different parameters:
32 and 8 bit CPU data bus width
clock divider ratio registers enabled/disabled
base time period normal/overdrive mode option pairs ("5.0", "1.0"), ("6.0", 0.5") and ("7.5", overdrive not implemented)
The Bash script can be modified to run a specific test. The parameter nested loop can be commented out and the last test will generate waveforms and open them in GTKWave.
## C driver tests

# License
Verilog RTL and testbench files are licensed under LGPL 3.
TCL scripts for integration into Altera tools is licensed under LGPL 3. This files were at first based on Altera demos, but are now entirely rewritten according requirements described in SOPC Builder documentation.
The glue code for the Nios II HAL is licensed under LGPL 3. This files were at first based on Altera demos, but are now entirely rewritten according requirements described in Nios II documentation.
The license for the "public domain kit" has not been change. The modified code is public domain.
# References

1-Wire Products Design Guide
http://www.maxim-ic.com/design_guides/en/1_WIRE_PRODUCTS_4.pdf

iButton Overview
http://pdfserv.maxim-ic.com/en/an/appibstd.pdf

1-Wire Public Domain Kit
http://files.dalsemi.com/auto_id/public/owpd310r2.zip
http://pdfserv.maxim-ic.com/en/an/AN1097.pdf
http://pdfserv.maxim-ic.com/en/an/AN155.pdf

DS18S20 1-Wire Parasite-Power Digital Thermometer
http://datasheets.maxim-ic.com/en/ds/DS18S20.pdf

DS18B20 Programmable Resolution 1-Wire Digital Thermometer
http://datasheets.maxim-ic.com/en/ds/DS18B20.pdf

SOPC Builder User Guide
4. SOPC Builder Components
7. Component Interface Tcl Reference
10. SOPC Builder Component Development Walkthrough
http://www.altera.com/literature/ug/ug_sopc_builder.pdf

Avalon MM
www.altera.com/literature/manual/mnl_avalon_spec.pdf

μC/OS-II
Jean J. Labrosse: MicroC OS II: The Real Time Kernel