1-wire (onewire) master
Verilog source with an Avalon MM processor interface

# Introduction
## 1-wire protocol and devices
The 1-wire protocol was defined by Dallas Semiconductor. In 2001 the company was bought by Maxim Integrated Products, Inc. Maxim is the sole manufacturer of 1-wire and iButton devices, all devices and standards can be found on their web-page:
http://www.maxim-ic.com/products/1-wire/
## Features
This document describes a 1-wire master written in Verilog HDL, ready for integration into a FPGA based SoC. Only the physical layer of the protocol is implemented in hardware, so only bit level data transfers are possible, a software driver is required to perform byte level transfers and to support protocol layers above the physical layer. Features:
1. reset pulse generation and presence detection, bit level write and read, timed idle slot
2. overdrive mode
3. from 1 to 16 wires
4. power (strong pull-up)
5. pulling or interrupt driven CPU interface
There are also other feature restrictions related to the design of the 1-wire bus (MicroLan). There are no features useful for handling a long and unstable bus, like active pull-up or adaptive timing.
# Verilog module parameters and ports
The next section describes how to properly integrate the Verilog module into an FPGA.
## Parameters
Table 1: List of onewire module parameters
parameter	type	default	range	description
CDR	integer	10	0, 1, ...	clock divider ratio
BDW	integer	32	8, 32	bus data width
OWN	integer		1, 2, ..., 16	number of wires

### Clock divider ratio
The internal state machine uses a reference period 7.5{%mu}s thus clock divider parameter is computed with the next formula:
CDR = f_{clk} cdot 7.5{%mu}s
If the dividing factor is not a round integer, than the timing of the controller will be slightly off, and would support only a subset of 1-wire devices with timing closer to the typical 30us slot. This limits the system clock to multiples of 133kHz.
f_{clk} = CDR cdot {400 over 3} "kHz" approx SDR cdot 133kHz
If overdrive is needed than the additional restriction is that CDR must be divisible by 10. This limits the system clock to multiples of 1.33MHz.
f_{clk} = CDR cdot {4 over 3} "MHz" approx SDR cdot 1.33MHz
TODO: if the system clock requirements can not be met, it is possible to recode the state machine to use 6{%mu}s reference periods, this way a better tolerance to divider ratio error can be achieved.
### Data bus width
The width of the data bus is 32bit by default, but only 8 bits are used, so it is possible to connect the controller to a 8bit CPU. The details are explained in the section on module ports.
## Ports
Table 2: List of onewire module ports
signal	width	direction	description
bus_write	1	input	bus write request
bus_read	1	input	bus read request
bus_writedata	BDW	input	bus write data
bus_readdata	BDW	output	bus read data
bus_interrupt	1	output	bus interrupt status
onewire_i	OWN	input	1-wire bus status
onewire_e	OWN	output	1-wire open collector driver enable
onewire_p	OWN	output	1-wire power enable (strong pullup)

### CPU bus interface
The default bus interface is 32bit Avalon MM compatible. It should be trivial to connect it to Wishbone and it should be easy to connect to AMBA APB. With the limitation to a single wire (OWN=0) the module can be also connected to an 8bit bus (a microcontroller for example). All CPU related signals are active high.
Both read and write cycles are a single clock period long, the omitted bus_waitrequest would be a constant '0'. Read data is valid only the first cycle of avalon_read being active, in the next cycle it might change due to the interrupt status being cleared.
The interrupt signal indicates, that a reset, presence detection, write bit or read bit 1-wire slots has finished. After performing a bus read the interrupt is cleared.

Drawing 1: Bus timing (write, read and interrupt status)

clk
bus_write
bus_read

bus_writedata
bus_readdata
bus_interrupt

The next table describes how to connect the 1-wire to an Avalon MM or Wishbone master.
Table 3: Wishbone equivalents of Avalon MM signals
bus signal	Avalon MM signal	Wishbone signal
bus_write	avalon_write	cyc & stb & we
bus_read	avalon_read	cyc & stb & ~we
bus_writedata	avalon_writedata	dat_w
bus_readdata	avalon_readdata	dat_r
bus_interrupt	avalon_interrupt	irq

### 1-wire interface
The 1-wire interface requires an external open drain driver to be able to drive a bidirectional FPGA pin. The next Verilog code should be used on the top level of the SoC.

assign owr = owr_oe ? 1'b0 : 1'bz;
assign owr_i = owr;
# Processor interface
The processor interface is described in two steps, status/control register description and action sequences.
## Registers

## Status/control register
There is a single register in the 1-wire master address space. This register is further restricted to only 8 bits. Writing into this register will always initiate an 1-wire slot. Writing into the register while a cycle is already in progress will break the running cycle and start a new cycle usually causing a protocol error.
Table 4: Statues/control register structure
	7	6	5	4	3	2	1	0
name	erx	etx	srx	stx	pwr	ovd	rst	dat
access	r/w	r/w	r	r	r/w	r/w	w	r/w
reset	0	0	0	0	0	0	0	x

Table 5: Status control register bits with descriptions
		description
0	dat	write: data transmit request (0 - perform write 0 slot, 1 - perform write 1 or/and read slot) / read: data receive status (read value for each 1-wire read slot) / read: presence detect status (0 - device presence detected, 1 - no device detected)
1	rst	write: reset pulse request (0 - no action, 1 - perform reset and read presence) / read: direct wire line status
0	ovd	overdrive setting (0 - standard speed, 1 - overdrive speed)
3	pwr	power supply (0 - normal operation, 1 - supply power over 1-wire)
4	stx	status of transmit interrupt (set on end of reset or write data slot, cleared by Avalon read)
5	srx	status of receive interrupt (set during presence or read data slot, cleared by Avalon read)
6	etx	enable transmit interrupt (0 - disabled, 1 - enabled)
7	erx	enable receive interrupt (0 - disabled, 1 - enabled)

Bits ovd, rst, dat are used to configure a slot. Bit ovd is used to specify the transfer speed. Combinations of this bits are used to select 8 different slot types. Detailed timing for this slots is explained in the section "Supported 1-wire functionality".
Table 6: List of supported slots
ovd	rst	dat	timing	description
0	0	0	60μs	write '0' cycle
0	0	1	60μs	write '1' cycle or read cycle
0	1	0	960μs	reset and presence detect cycle
0	1	1	960μs	timed idle cycle, can be used to generate timed delays
1	0	0	6μs	overdrive write '0' cycle
1	0	1	6μs	overdrive write '1' cycle or read cycle
1	1	0	96μs	overdrive reset and presence detect cycle
1	1	1	0μs	untimed idle cycle, can be used to change power settings

Bit dat has a different meaning for write than for read. When read it contains the presence status for a reset cycle or read data status for a read bit cycle.
Bit rst has a different meaning for write than for read. When read it simply shows the line state, which might be useful for debugging.
Bits stx, srx describe the current state of a slot. Each slot has a read-point when srx is set and an end-point when stx is set, the slot is completed and a new slot can be issued. Both bits are cleared by a register read, so care must be taken to check their value after every read. For pooling it is usually enough to check the end-point status bit stx, for interrupt driven software it might be useful to detect the read-point status bit srx too.
Bits etx, erx specify if stx, srx will trigger an interrupt or not. Their usage depends on the implementation of the driver.
## Action sequences
The 1-wire master can be used to perform most actions defined in the iButton specification as the physical layer. It is possible to use pooling or interrupts, both options will be described.
The description uses the next pseudo functions:
- write (data) - 8bit (16bit or 32bit) write to the configuration/status register
- data = read () - 8bit (16bit or 32bit) read from the configuration/status register
### Pooling
Pooling is not an optimal implementation, but it might be useful for debugging purposes. Since interrupts are not used '0' should be written into interrupt enable registers and interrupt status registers are used to identify the end of the cycle.
#### Reset
A '1' is written into the rst bit and a '0' is written into the txd bits. Bit ovd is used to select normal or overdrive speed. The software must wait in a loop till the cycle ends (alternatively it is possible to first wait for the read-point an than for the end-point) and than the presence status can be read from bit rxd. The next function returns the presence detect status.
bool reset (bool overdrive) {
  write (0x02 | overdrive);
  while ((reg = read()) & 0x20);
  return (reg & 0x08);
}
#### Write bit
A boolean value bit is written into the txd bit, this will cause a write bit cycle on the 1-wire bus. Bit ovd is used to select normal or overdrive speed. The software must wait in a loop till the cycle ends (alternatively it is possible to first wait for the read-point an than for the end-point) and than the presence status can be read from bit rxd.
void write_bit (bool bit, bool overdrive)
  write ((bit<<3) | overdrive);
  while ((reg = read()) & 0x20);
  return;
}
#### Read bit
A '1' is written into the txd bit, this will cause a read (write '1') cycle on the 1-wire bus. Bit ovd is used to select normal or overdrive speed. The software must wait in a loop till the cycle ends (alternatively it is possible to first wait for the read-point an than for the end-point) and than the read bit status can be read from bit rxd. The next function returns the read bit status.
bool read_bit (bool overdrive) {
  write (0x02 | overdrive);
  while ((reg = read()) & 0x20);
  return (reg & 0x08);
}
# Supported 1-wire functionality

# SOPC builder integration
# Software driver