1-wire (onewire)

# Introduction
## 1-wire protocol and devices
The 1-wire protocol was defined by Dallas Semiconductor. In 2001 the company was bought by Maxim Integrated Products, Inc. Maxim is the sole manufacturer of 1-wire and iButton devices, all devices and standards can be found on their web-page:
http://www.maxim-ic.com/products/1-wire/
## Features
This document describes a 1-wire master written in Verilog HDL, ready for integration into a FPGA based SoC. Only the physical layer of the protocol is implemented in hardware, so only bit level transfers are possible, a software driver is required to perform byte level transfers and to support protocol layers above the physical layer. Features:
1. reset pulse generation and presence detection
2. bit level write and read
3. overdrive mode
4. pulling or interrupt driven CPU interface
There are also other feature restrictions related to the design of the 1-wire bus (MicroLan). There are no features useful for handling a long and unstable bus, like active pull-up or adaptive timing.

# Verilog module parameters and ports
The next section describes how to properly integrate the Verilog module into an FPGA.
## Parameters

parameter	type	default	description
CDR	integer	10	clock divider ratio
ADW	integer	32	Avalon data width

### Clock divider ratio
The internal state machine uses a reference period 7.5{%mu}s thus clock divider parameter is computed with the next formula:
CDR = f_{clk} cdot 7.5{%mu}s
If the dividing factor is not a round integer, than the timing of the controller will be slightly off, and would support only a subset of 1-wire devices with timing closer to the typical 30us slot. This limits the system clock to multiples of 133kHz.
f_{clk} = CDR cdot {400 over 3} "kHz" approx SDR cdot 133kHz
If overdrive is needed than the additional restriction is that CDR must be divisible by 10. This limits the system clock to multiples of 1.33MHz.
f_{clk} = CDR cdot {4 over 3} "MHz" approx SDR cdot 1.33MHz
TODO: if the system clock requirements can not be met, it is possible to recode the state machine to use 6{%mu}s reference periods, this way a better tolerance to divider ratio error can be achieved.
### Data bus width
The width of the data bus is 32bit by default, but only 8 bits are used, so it is possible to connect the controller to a 8bit CPU. The details are explained in the section on module ports.
## Ports

signal	width	direction	description
avalon_write	1	input	Avalon MM write request
avalon_read	1	input	Avalon MM read request
avalon_writedata	ADW	input	Avalon MM write data
avalon_readdata	ADW	output	Avalon MM read data
avalon_interrupt	1	output	Avalon MM interrupt status
owr_i	1	input	1-wire bus status
owr_oe	1	output	1-wire open collector driver enable

### CPU bus interface
The default bus interface is Avalon MM, but it is trivial to connect it to Wishbone and it should be easy to connect to AMBA APB. All CPU related signals are active high.
Both read and write cycles are a single clock period long, the omitted "avalon_waitrequest" would be a constant "0". Read data is valid only the first cycle of "avalon_read" beeing active, in the next cycle it might change due to the interrupt status being cleared.
The interrupt signal indicates, that a reset, presence detection, write bit or read bit 1-wire transaction has finished. After performing a read on the CPU bus the interrupt is cleared.

clk
avalon_write
avalon_read

avalon_writedata
avalon_readdata
avalon_interrupt

The next table describes how to connect the 1-wire Avalon MM slave to a Wishbone master.
Avalon signal	Wishbone signal
avalon_write	cyc & stb & we
avalon_read	cyc & stb & ~we
avalon_writedata	dat_w
avalon_readdata	dat_r
avalon_interrupt	irq

### 1-wire interface
The 1-wire interface requires an external open drain driver to be able to drive a bidirectional FPGA pin. The next Verilog code should be used on the top level of the SoC.

assign owr = owr_oe ? 1'b0 : 1'bz;
assign owr_i = owr;
# Processor interface
The processor interface is described in two steps, status/control register description and action sequences.
## Status/control register
There is a single register in the 1-wire master address space. This register is further restricted to only 8 bits.

	7	6	5	4	3	2	1	0
name	erx	etx	srx	stx	drx	dtx	rst	ovd
access	r/w	r/w	r	r	r	w	w	r/w
reset	0	0	0	0	x	x	0	0

		description
0	ovd	overdrive setting (0 - standard speed, 1 - overdrive speed)
1	rst	reset pulse request (0 - no action, 1 - perform reset and read presence)
2	dtx	data transmit request (0 - perform write 0 transfer, 1 - perform write 1 or/and read transfer)
3	drx	data receive status (read value for each 1-wire read transfer)
4	stx	status of transmit interrupt (set on the end of a reset or bit cycle, cleared by Avalon read)
5	srx	status of receive interrupt (set during presence or read bit cycle, cleared by Avalon read)
6	etx	enable transmit interrupt (0 - disabled, 1 - enabled)
7	erx	enable receive interrupt (0 - disabled, 1 - enabled)

## Action sequences
The 1-wire master can be used to perform most actions defined in the iButton specification as the physical layer.

# Supported 1-wire functionality

# SOPC builder integration
# Software driver